## Slide 1: CIE 4400 Water Quality Modeling Completely & incompletely mixed systems
Saket Pande

## Slide 2: Completely mixed systems
  Water mass balance
  +
  Pollutant mass balance
Notes: What are the inputs, outputs ? Think of all hydrological terms!

## Slide 3: Fundamental equation (one dimensional)
∆x
Jout
Jin
W
Ac
Mass Balance of water
Mass Balance of pollutants
∆V: Volume of differential element (L3)
Jin: Ingoing mass flux rate (ML-2/T)
Jout: Outgoing mass flux rate (ML-2/T)
Ac: Cross sectional area (L2)
∆x: Length of differential element (L) = ∆V/ Ac
c: concentration of the pollutant (ML-3)
Accumulation = Inflow – Outflow– Reaction + Loading

## Slide 4: Basic water balance assumptions (unless specified otherwise)
Water mass balance is at steady state (unless specified otherwise), i.e.
If we further assume that W = 0 (i.e. no additional source of water except inflow and outflow)
, or
Once Q is given, we need not worry about water mass balance under such assumptions.

## Slide 5: Some definitions
Mass loading rate (W): Mass m (M) of pollutant entering the system over time period t (T), W [MT-1] = m/t
  Point sources
Volumetric flow rate (Q):Water with average velocity U (LT-1) entering the system perpendicular to cross sectional area Ac (L2), Q [L2T-1] = U Ac
Mass flux rate (J): Loading rate per unit cross sectional area, J [MT-1L-2] = W/ Ac

## Slide 6: Completely mixed systems
  Different from water mass balance ?
Well-mixed
reservoir
Inputs State variables Outputs
Outflow
Settling
Reactions
Accumulation = Inflow – Outflow – Reaction – Settling + Loading
Loading
Inflow
Notes: Precipitation, evaporation and infiltration into the subsoil included in the loading / outflow

## Slide 7: Loading types in the pollutant balance
Accumulation =Inflow – outflow - settling – reaction + Loading
Impulse loading (W = W0δ(t)): W0 is the mass loading rate of pollutant entering the system over a relatively short period of time. Here δ(t) is a dirac delta function
  Accidental spill
Step Loading (new continuous source): When loading rate changes from 0 to a constant value at some point in time.
  Pollution from industrial activities (eg chemical plants)
Pulse loading (difference between two step loadings starting at different times): Loading rate jumps from 0 to a constant for a period of time and then jumps back to zero.
  Start and end of an industrial pollution activity.

## Slide 8
Impulse loading?
Step loading?
Pulse loading?

## Slide 9: Reaction kinetics
Reaction kinetics
  Zero, first or second order?
C(t)
t
1/C(t)
t
ln(C(t)
t

## Slide 10: Reaction kinetics
First order reactions are only considered in this class
Time scale of the process
1 / k
C0
C(t)
Time t

## Slide 11: SUMMARY
Mass balance of a pollutant
- Accumulation is the change in pollutant stored in a control volume V:
- often is not distinguished from W. So beware!
Accumulation = Inflow – outflow - settling – reaction + Loading

## Slide 12: Completely mixed systems
How about:
  Susceptibility of a system to pollution?
    steady state analysis, i.e. when
  Time to recovery after pollutant loading?
    Solution of a linear differential equation

## Slide 13: Susceptibility to pollution (steady state)
Completely mixed system at steady-state
Higher assimilation factor, less susceptible to pollution
where a is called assimilation factor that depends on the outflow rate, reaction kinetics of the system, settling velocity and settling area. Thus the assimilation factor partly depends on the intrinsic properties of a system.
Notes: Well discussed in Chapra’s book,
assimilative capacity
Definition
Capacity of a natural body of water (lake, river, sea, etc.) to receive waste waters or toxic materials, without harmful effects and damage to aquatic life and to humans who consume its water.

## Slide 14
End of hour 2

## Slide 16: Residence time of pollutants (steady state)
(Mean) Residence time:
  - residence time of lake water :
  mean residence time of pollutant x: quantity of pollutant (either mass or concentration) in the control volume/absolute value of sources or sinks:

## Slide 17: Transfer function of a completely mixed system (steady state)
c
c
Q
Q
Lake’s removal mechanisms reduce pollution
Small assimilative capacity of the lake
If
where
So when,
Notes: Low beta = high a compared to Q
Note: Q appears in the numerator and denominator; it represents delivery (inflow) as well as flushing (outflow)

## Slide 18: Pollutant reduction (transient analysis)
Pollutant reduction for step load function
  - Load decreases: time to recovery? Shape of recovery?
W(t)
t
t0
c(t)
t
Time to recovery
Shape of recovery
a
b
c
t0
Notes: What do you think? a of b of c?

## Slide 19: For further analysis we need the solution for..
Solution:

## Slide 20: Pollutant reduction from an arbitrary loading
Determinant of the shape of recovery from an arbitrary load function
λ is the determinant of the shape of recovery from any arbitrary load function.
We use λ interchangeably with

## Slide 21: Pollutant reduction
How the system behaves once the load stops completely at t = t0 (pulse load) with the concentration of the system at c0 ?
C(t)
t
c10
t10
t0
c0
For t>t0
What time concentration of the system reached 10% of c0?

## Slide 22: Pollutant reduction: Solutions for different loading functions
  Solutions for particular functional forms of W(t)
    Impulse load
    Step load
W(t)
t
W(t)
t

## Slide 23: Pollutant reduction: impulse load
  Impulse load ()= load that stops immediately
c(t)
t
m0/V
t0
Solution:

## Slide 24: Pollutant reduction: step load
  Step load = continuous load after t0, i.e.
C(t)
t
Wcst /(λV)
t0
Solution:

## Slide 25: Pollutant reduction
Solution for arbitrary load
    Assumption: linear system (show that we have been working with a linear system!)
      effect (load 1 + load 2) = effect (load 1) + effect (load 2)
      effect (2 * load 1) = 2* effect (load 1)
W(t)
t
C(t)
C(t)
Sum them up

## Slide 26: Pollutant reduction
Solution for arbitrary load
W(t)
t
C(t)
C(t)
Convolution
response
= response of impulse unit loading
Impulse loading
t
What is the impulse response of a system governed by the following equation?

## Slide 27
End of hour 3

## Slide 28: Incompletely mixed system

## Slide 29: A conceptual model for diffusion
A feedback system with equal volumetric flow D’ (similar to λ?) in both the directions
Two well mixed reservoir of constant volume V
D’
D’
c1
c2
V

## Slide 30: Ficks first law for diffusion
Mass flux is proportional to the gradient of concentration with a sign opposite to that of the gradient
or

## Slide 31: Further scrutiny of Fick’s law
D’
D’
c1
c2
V
Ac
Discretize Fick’s law for the above case:
Apply conservation of mass to the left reservoir:

## Slide 32: What is diffusion/dispersion coefficient?
Represents the intensity of mixing
Depends on “mixing length” and cross sectional area of mixing
Therefore scale dependent
D’
D’
c1
c2
V
=D’ )
D=
Ac

## Slide 33: Variants of diffusion
Diffusion
Dispersion
Conduction
Convection

## Slide 34: Diffusion coefficients
Source: Book Chapra
cm2/s
Turbulent diffusion coeff.: property of the fluid
Dturb >>Ddiff (eddies >> larger than molecule motion)

## Slide 35: Types of spills
Instantaneous point spill: a spill (or loading) at one instance in time and one point in space
Continuous point spill: a spill continuous in time but at one point in space
Instantaneous nonpoint/distributed spill: ?
Continuous nonpoint/distributed spill: ?

## Slide 36: Fundamental equation (one dimensional)
∆x
Jout
Jin
W
Ac
Mass Balance of water
Mass Balance of pollutants
∆V: Volume of differential element (L3)
Jin: Ingoing mass flux rate (ML-2/T)
Jout: Outgoing mass flux rate (ML-2/T)
Ac: Cross sectional area (L2)
∆x: Length of differential element (L) = ∆V/ Ac
c: concentration of the pollutant (ML-3)

## Slide 37: Diffusion (or Dispersion or Convection) equation for a differential element
∆x
Jout
W
Ac
Jin
; =?
Why?

## Slide 38: Creating an ordinary differential equation from a differential element
Formulate diffusion equation with a first order decay equation and W = 0 (in groups)
What if W>0 but a point source ? (in groups)
As ,
∆x
Jout
W
Ac
Jin

## Slide 39: Steady state solution for diffusion equation with decay
Let a system be really large, ranging from to [L]. Let the concentration at x = 0 be c0.

## Slide 40: Molecular Diffusion (feel it)
Evolution of a colored droplet on lake surface
  What happens to concentration?
  (in groups)
x
y
Top view
t0
t1
t2
x
at t1, at t2?
c(x)

## Slide 41: Advection only
Center of mass of a differential pollutant mass flows with constant velocity U
1D plug flow model
wasteload
river
ideal plug flow
real profile
Time step t0
Time step t1

## Slide 42: 1D Plug Flow Model
Formulate the differential equation for reaction = k∆Vc, and W= 0
Ac
cin
cout
Q
Q
; =?
∆x

## Slide 43: Steady state solution for 1D plug flow model with first order kinetics
Let c(t, x=0) = c0
X (m)
c(x) (mg/L)
For example:
c0=1mg/L, k= 2/hr, U = 100 m/hr, Ac = 10 sq m, L = 100 m
Steady state
solution?

## Slide 44: Why c0 = W/Q under no diffusion when the point (continuous) loading at x = 0 is W
Differential element, well mixed and at steady state
x=0
If and then

## Slide 45: Cascade Model of an elongated tank
Feed forward system with first order decay at steady state
∆x
A well mixed reservoir of volume V
cin
cout
Q
Q
n well mixed reservoirs
Solution:

## Slide 46: Cascade Model: feedforward system of completely mixed tanks
When is cascade model equivalent to 1D plug flow model ?
c(x) (mg/L)
X (m)
If V is the total control volume and there are n=6 well mixed reservoirs.
Concentration in the jth reservoir is given by:
Cascade model
Plug Flow model

## Slide 47: Approximating incompletely mixed condition by piecewise completely mixed systems
Fundamental to modeling heterogeneous concentration fields
  For example: cascade model approached plug flow model at n →∞.
How is the formulation of a cascade model different from Plug flow model formulation?

## Slide 48: Extending the completely mixed system model
Incomplete mixing: network of box models
Water compartments
Fluxes between compartments ?

## Slide 49: Mixed flow model (Advection + Dispersion)
Advective and dispersive fluxes are additive.
Formulate the mass balance equation (in groups)
cin
cout
Q
Q
∆x
Ac
Solution:

## Slide 50: ADE equation with first order decay process
1) How would the concentration distribution propagate when some instantaneous point spill leading to c(x=0,t=0)=c0 and no reactions or additional loading? (in groups)
c
x

## Slide 51: Steady state solution for Mixed flow model
Obtain steady state solution for Plug flow model from this?
Due to point (continuous) loading W(x) = Wδ(0) at x = 0

## Slide 52
End of hour 4