## Slide 1: Model Calibration and Uncertainty
Markus Hrachowitz
m.hrachowitz@tudelft.nl
Room 4.87

## Slide 2: After this lecture you will
be able to describe sources of uncertainty in hydrological models
be able to identify and classify model parameter calibration procedures
be able to explain and discuss different model performance measures
be able to analyze and assess different model evaluation techniques
Objectives
Sources of uncertainty
Why do we care?
Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 3: Hydrological models
Q←m(X,, S0)
  Q: system response
  m: hydrological model
  X: inputs
  : model parameters
  S0: initial and boundary conditions
Each component is subject to uncertainty
 Objectives
Sources of uncertainty
Why do we care?
Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 4: Sources of uncertainty
Low precision High accuracy
High precision Low accuracy
Example:
Catchment 5km2,
6 rain gauges
Proportion of rain gauges that record rain when one of them is recording rain
 Objectives
Sources of uncertainty
Why do we care?
Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?
Observational uncertainty
(i) instrument precision
(ii) measurement accuracy
(iii) spatial and temporal heterogeneity
(How representative is the measurement?)
Present in:
(i) input (e.g. rain, evaporation)
(ii) response (runoff, groundwater, chemical composition)
Model structure uncertainty
Imperfect conceptualization of system
Model parameter uncertainty
Different parameter combinations can yield same result

## Slide 5: Error propagation in catchment modelling
True forcing inputs
Forcing data errors
Observed forcing data
CATCHMENT MODEL
Model structure error
Simulated response
Observed response
True response
Response data errors
True dynamics
Model parameters
error
 Objectives
 Sources of uncertainty
Why do we care?
Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?
≠
!!!

## Slide 6
Parameter estimation
Q← m(X,,S0)
Direct measurement (problem of scale)
Derivation from analysis of measured variables (problem of scale, uniqueness of place)
Calibration
 Objectives
 Sources of uncertainty
 Why do we care?
Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 7
Calibration
Calibration is a process of parameter adjustment (automatic or manual), until observed and calculated output time-series show a sufficiently high degree of similarity
Model parameters are conceptual representations of abstract watershed characteristics - not independently measurable
 Objectives
 Sources of uncertainty
 Why do we care?
Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 8
Manual calibration
Also called “Trial-and-error”
Based on:
a) Visual inspection of the hydrograph
b) Different measures of performance
Can produce good results but:
a) time consuming
b) not objective
 Objectives
 Sources of uncertainty
 Why do we care?
Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 9
Automatic calibration
Computer based
Fast
Objective
but
The resulting hydrographs are often perceived to be inferior to those produced through manual calibration from the hydrologist’s point of view
 Objectives
 Sources of uncertainty
 Why do we care?
Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 10
Automatic calibration
Parameter calibration problem is set as an optimization problem
Optimization means finding the parameters that maximise or minimise a certain function
Model performance is expressed as a function of model parameters (objective function N)
Qm = m(X,,S0)
Qo : observed system response
Nobj=f(Qm,Qo)
 Objectives
 Sources of uncertainty
 Why do we care?
Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 11
Objective functions
Objective functions aggregate model residuals in time
Different functions can express the error associated to different aspects of the simulation (e.g. high flow, low flow, bias, groundwater dynamics)
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 12
Bias !
Bias !
Coefficient of determination
(timing, 0 ≤ R2 ≤ 1)
Nash-Sutcliffe efficiency
(high flow, 0 ≤ NS ≤ 1)
Log Nash-Sutcliffe efficiency
(low flow, 0 ≤ logNS ≤ 1)
Mean square error
(high flow, 0 ≤ MSE ≤ ∞)
Bias (0 ≤ Bias ≤ ∞)
Objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 13
Optimization of objective functions
How does the response surface of objective function Nobj=f() look like?
  Complex landscapes with multiple curving ridges
  Small- and large-scale discontinuities
  Multiple optima
1
2
Nobj
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 14
Search strategies for finding optimal parameter set
Local search strategies can converge in a local minimum instead of the global one
Solved with global search strategies that use randomized search
1
2
Nobj
Local minima
Global minimum
Optimization of objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 15
Global search strategies for finding optimal parameter set:
Stochastic
(a) Monte-Carlo sampling,
(b) Simulated annealing,…
Heuristic
(a) Genetic algorithms,
(b) Shuffled Complex Evolution,
(c) Ant-Colony and Particle Swarm methods,…
Optimization of objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 16
Monte Carlo Sampling
Randomly sample each parameter from prior distribution
Very simple
Time consuming
Although good information about the region of optimal parameters, best parameters unlikely to be found
Optimization of objective functions
Nash-Sutcliffe Efficiency
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 17
Evolutionary algorithms
Optimization of objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 18
Evolutionary algorithms
Optimization of objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 19
Evolutionary algorithms
Optimization of objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 20
Evolutionary algorithms
Optimization of objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 21
Evolutionary algorithms
Optimization of objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 22
Evolutionary algorithms
Optimization of objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 23
Evolutionary algorithms
Optimization of objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 24
Evolutionary algorithms
Optimization of objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 25
Optimization of objective functions
Ant-Colony optimization
Mimics self-organizing dynamics of nature
Based on collective “intelligence” of insects
Collective of ants finds shortest route to food
Leave pheromone trail, attracting other ants
The more ants, the more pheromone, the more ants  positive feedback process (self-organization)
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 26
Optimization of objective functions
Complex shape of objective functions can be a numerical artifact
Remember exercise 1
Using a too large time step introduces large numerical error
This can affect the shape of the objective function
1. Fixed-step explicit Euler
2. Adaptive substepping
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 27
Optimization of objective functions
Multiple optima
Response surface can have more than one optimum
Many parameter sets may yield equally good results
This has impact on parameter and predictive uncertainty
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 28
Parameter uncertainty
Multiple optima – different approaches
Accept existence of multiple optima and introduce concept of equifinality (GLUE)
Use of Bayesian statistics to address in a formal way problems related to data uncertainty
Accept that a single objective function is not appropriate: instead use more criteria and objectives to constrain the problem (Multi-criteria, multi- objective calibration)
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 29
Parameter uncertainty
GLUE
(Generalized Likelihood Uncertainty Estimation)
“The concept of a single description of reality may remain a philosophical axiom or theoretical aim but is impossible to achieve in practice”
“So we must accept that there may be many feasible descriptions, or a concept of equifinality, as the basis for a new approach”
(Keith Beven)
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 30
Parameter uncertainty
GLUE
(Generalized Likelihood Uncertainty Estimation)
Rejects the concept of an optimum model and parameter set
The existence of multiple likely models and parameter sets has been called equifinality
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 31
Parameter uncertainty
GLUE
(Generalized Likelihood Uncertainty Estimation)
(1) Prior to input of data into a model, all model structures and parameter sets have an equal likelihood of being acceptable
(2) A high number of parameter sets is generated via uniform Monte Carlo sampling
(3) The performance of each trial is assessed through a likelihood measure (e.g. Nash-Sutcliffe Efficiency)
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 32
Parameter uncertainty
GLUE
(4) Only models, i.e. parameter sets and model structures, whose likelihood measure is above a threshold are retained (“behavioural models”), all others are discarded (“non-behavioural models”)
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 33
Parameter uncertainty
GLUE
(5) The calculated likelihoods are rescaled to a cumulative sum of 1
(6) For each time step, a cumulative distribution of simulated discharges is constructed using the rescaled weights
(7) Uncertainty bounds and median from cumulative distribution
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 34
Parameter uncertainty
GLUE – example
10 km2 catchment in Scotland
Modelling tracer dynamics in stream
2 parameter model (α,β)
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 35
Parameter uncertainty
GLUE – example
Likelihood measure: Nash-Sutcliffe efficiency (NSE)
Threshold of acceptance: NNS > 0.6
“behavioral models” - retained
“behavioral models” - retained
“non-behavioral models” - discarded
“non-behavioral models” - discarded
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 36
GLUE – example
Parameter uncertainty
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 37
GLUE
Glue introduces the problem of equifinality in hydrological modelling
Easy to understand and implement
Allows model evaluation with respect to performance and uncertainty
Limitation: subjectivity (choice of threshold!)
To limit subjectivity:
(a) “Limits of acceptability” approach
(b) Adjust threshold so that x% of observations fall within uncertainty interval
(c) Accept all models, but give higher weight to better models, e.g. NSEp
Parameter uncertainty
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 38
Formal Bayesian approach
Likelihood functions should be based on hypotheses of the error
Example:
Qo,i = Qm,i+ εi
εi ~ N(μ=0; σ2)
Parameter uncertainty
Qo
εi
Qm
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 39
Formal Bayesian approach
Qo,i = Qm,i+ εi
εi ~ N(μ=0; σ2)
Parameter uncertainty
Qo
εi
Qm
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 40
Formal Bayesian approach
For Bayesian statistics estimating θ using least squares means adopting several assumptions:
(a) model is correct
(b) error is normally distributed, uncorrelated, with constant variance (homoscedastic) and zero mean
Parameter uncertainty
Qo
εi
Qm
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 41
Multi-objective calibration
Data contain different signatures of catchment behaviour
Information contained in the data represented by a single number
Information represented by this number is then transferred to the model parameters
Ideally parameter dimension should be the same as objective function dimension
Parameter uncertainty
Data
Objective
function
Parameters
Dimension
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 42
Multi-objective calibration
Acceptable parameter range can be constrained by defining multiple optimization targets:
(a) Multiple objective functions (objectives), e.g. NS, NSlog, R2, to evaluate one single modelled time-series, e.g. streamflow
(b) Objective functions to evaluate multiple modelled variables (criteria), e.g. stream flow, groundwater, chemical composition
(c) Objective functions in the frequency domain, e.g. fit flow duration curves or frequency spectrum
(c) Combinations of (a), (b) and (c)
Parameter uncertainty
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 43
Parameter uncertainty
Multi-objective calibration
Pareto Optimality
Not possible to find two points within the Pareto set such that one has a better performance than the other with respect to all objective functions
For all non-members there exists at least one member that has a better performance with respect to all objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?
Parameter
Objective function F (a)

## Slide 44
Parameter uncertainty
Multi-objective calibration: Pareto Optimality
Pareto Solutions
(e.g. 1-NS)
(e.g. 1-NSlog)
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 45
Parameter uncertainty
Multi-objective calibration
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 46
Parameter uncertainty
Multi-objective calibration: Example
HBV model
3 objective functions
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 47
Parameter uncertainty
Multi-objective calibration: Example
NHF, NLF and NWT
NHF and NLF
Parameter ranges
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 48
Parameter uncertainty
Multi-objective calibration: Example
NHF, NLF and NWT
NHF and NLF
Hydrograph
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 49
Parameter uncertainty
Multi-objective calibration: Example
Groundwater table
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 50
Parameter uncertainty
Multi-objective calibration
Takes into account the multi-objective nature of the calibration problem
Takes into account that different parts of the hydrograph can be subject to different error processes
Reflects the model’s inability to correctly and simultaneously simulate different aspects of the simulations
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
Parameter uncertainty
New approaches
What have we learned?

## Slide 51
Stepped Calibration Approach
(1) Select different specific characteristics of the time series that should be well simulated, e.g. high and low flow.
(2) Associate model parameters with the selected characteristics
(3) Define objective functions that represent performance measures for modelling the selected characteristics
(4) Calibrate each group of parameters associated with each objective function individually, while fixing the remaining parameters at constant values
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
New approaches
What have we learned?

## Slide 52
Stepped Calibration Approach
Example:
Calibration of stream flow with respect to high and low flows, i.e. NS and logNS
The optimal models related to two objective functions are different and both unrealistic
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
New approaches
What have we learned?

## Slide 53
Stepped Calibration Approach
Example:
First calibrate the groundwater related parameters, i.e. low flow, and then the others. The baseflow simulation remains almost unchanged
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
New approaches
What have we learned?

## Slide 54
Stepped Calibration Approach
Recognizes that results obtained by single objective calibration can be unrealistic
Tries to emulate the steps followed by hydrologists in manual calibration
Provides a balanced, physically realistic solution
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
New approaches
What have we learned?

## Slide 55
Dynamic Identifiability Analysis
Analyses parameter identifiability in a moving
time window:
(1) allows analysing how different regimes influence identifiability of model parameters
(2) allows investigating the assumption that model parameters are constant in time
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
New approaches
What have we learned?

## Slide 56
Dynamic Identifiability Analysis
Sample feasible parameter space
(2) Construct cumulative parameter distribution functions
(3) Evaluate parameter identifiability for each time step
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
New approaches
What have we learned?

## Slide 57
Dynamic Identifiability Analysis
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
New approaches
What have we learned?

## Slide 58
Dynamic Identifiability Analysis
Parameter Nlagf, which represents the lag time of the system, is non-stationary, i.e. it decreases with time
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
New approaches
What have we learned?

## Slide 59
Dynamic Identifiability Analysis
It allows analyses of parameter identifiability in time
It is useful to enhance model structural limitations
It can help to detect regimes with higher information content than others for specific parameters
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
New approaches
What have we learned?

## Slide 60
Current view on model evaluation
Requirements for model application:
  Model parameters have to be well identifiable
  The model has to be able to adequately reproduce the observations
  The model has to be a realistic representation of the natural system
Requirements for model evaluation:
  Evaluate the model with respect to the above mentioned aspects
  Identify the effect of various sources of error on model predictions and parameters
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
 New approaches
What have we learned?

## Slide 61
Current state
At present no unique framework for the evaluation of all aspects related to model evaluation
Different approaches could be combined based on the requirements of the specific problem
 Objectives
 Sources of uncertainty
 Why do we care?
 Calibration
 Objective functions
 Optimization
 Parameter uncertainty
 New approaches
What have we learned?