## Slide 1: Distributed modelling
CIE4431 – Hydrological Modelling
Remko Nijzink (with slides from Tanja Euser & Hessel Winsemius)
26 February 2016

## Slide 2: Today’s Topics
Why to use distributed models?
What are distributed models?
When and how to use distributed modelling?
Data sources

## Slide 3: Introduction
lumped vs distributed

## Slide 4: Introduction
lumped vs (semi) distributed
Lumped
Lobith
Semi-distributed

## Slide 5: Introduction
Advantages
  Fast
  Easy to implement
Disadvantages
  only the outlet (discharge) behaviour or lumped over whole catchment
  No internal info  no coupling with e.g. soil erosion or vegetation models
  Loss of information on spatial distribution
Lumped

## Slide 6: Introduction
Advantages
  Include distributed data sources (e.g. rainfall)
  Include distributed scenarios (e.g. land use change)
  Interpret distributed results (e.g. local erosion potential, vegetation changes, include local pollution sources)
Disadvantages
  Slower
  Equifinality (i.e. distribution of parameters often causes confusion and not necessarily a better model)
Fully distributed

## Slide 7: Introduction
Advantages
  Include distributed data sources (e.g. one rain gauge per sub-catchment)
  Fast
Disadvantages
  Little internal info
  Equifinality
Semi-distributed

## Slide 8: Introduction
  Distributed data available, so why not use it?
    Drivers
    Land use
  Known variability in hydrological processes
  Evaluate water balance in specific sub-domains
  We have a certain question that can only be answered with a distributed model:
    …
    …
Reasons to model distributed

## Slide 9: Introduction
But, be careful!
Extra information can be 'fake'
  How good is your distributed input data?
  Can you test your results?
Equifinality
Reasons to model distributed

## Slide 10: What are distributed models?
"Distributed refers to any selection of model structure, parameters or data which is not considered representative for the entire catchment "
What do they consist of?
A (conceptual or physical) model for the water balance
  input: rainfall, potential evaporation;
  output: evaporation, river discharge, etc.
Often some form of (river) routing

## Slide 11: What are distributed models?
Water balance model

## Slide 12: What are distributed models?
Water balance model
Each cell has:
  Input (e.g. rainfall)
  State variables (e.g. soil
  moisture, groundwater level)
  Output (e.g. evaporation, runoff)
Groundwater outflow goes straight to the river?
What to do with the runoff?
Rainfall
Evaporation
River discharge
Storage dynamics

## Slide 13: What are distributed models?
Water balance model
Rainfall
Evaporation
River discharge
Storage dynamics
grid
cell
Runoff (according to flow direction)

## Slide 14: What are distributed models?
Routing

## Slide 15: What are distributed models?
Runoff moves horizontally over the drainage network
Transport in a cell without storage consideration is:
where
n : location of upstream cell
i : location cell under computation
n = 0: the location of a water divide
Routing

## Slide 16: What are distributed models?
Taking into account that there is channel storage
  Kinematic wave approximations
Routing

## Slide 17: What are distributed models?
Routing

## Slide 18: What are distributed models?
(Fully-)distributed: grid with usually equal cell-sizes
  Gridded rainfall data
Semi-distributed: aggregation of grid-cells in spatial units e.g.:
  Location of runoff gauges
  According to Strahler order river network
  Hydrotope analysis (in between semi-distributed and distributed)
    Similar landscape elements
    Similar land use elements
    Similar ecosystem elements
Semi-distributed modelling

## Slide 19: Semi-distributed modelling
Strahler order

## Slide 20: Semi-distributed modelling
Example: Kabompo, strahler threshold?
Catchment boundary
Lumwana river (4th order stream)

## Slide 21: Semi-distributed modelling
Example: Kabompo, strahler threshold?
Catchment boundary
Kabompo river
(5th order stream)

## Slide 22: Semi-distributed modelling
Example: Kabompo, strahler threshold?
Catchment boundary
Kabompo river (8th order stream)

## Slide 23: Semi-distributed modelling
Areas (classes) of assumed similar hydrological behaviour
Remotely sensed/distributed data for delineation
Expert judgment or field examinations recommended
Also known as:
  Landscape units
  Hydrotopes
  Representative watersheds
  Classes
  Etc…
Hydrological response units

## Slide 24: Hydrological response units
Example Volta basin
slopes
plateaus
wetlands

## Slide 25: Hydrological response units
Use thresholds to derive the classes
Normalized Difference Vegetation Index (NDVI)
Logical expression:
If NDVI > 0.05, wetland
LandSAT imagery

## Slide 26: Hydrological response units
Use thresholds to derive the classes
Slope of topography
Logical expression:
If slope > 0.04, hill
DEM: slopes

## Slide 27: Hydrological response units
1. Plains (DEM)
2. Wetlands (NDVI)
3. Rivers (runoff)
4. Slopes (DEM)
Classification

## Slide 28: How and when to use distributed modelling?
Investigate what information you have available
Decide what is suitable to distribute and to what extend
  Data availability
  Which processes are you interested in?
  Area extent
Use the right tools:
  Computational time
  Programming language/framework
  Existing models
To start with

## Slide 29: How and when to use distributed modelling?
Distribution of input data
Distribution of model
  Distribution of parameters
  Distribution of model structure
Possibilities
 | Lumped model | Distributed model
Lumped data | Most simple | 
Distributed data |  | Most complex
Notes: Example interception on blackboard

## Slide 30: Distribution of input data
Data availability main issue
Heterogeneity of rainfall
Filtering in heterogeneity by model

## Slide 31: Distribution of parameters
Often combined with distribution of input data
Not all parameters distributed
  Landuse often suitable
  Make sure you can justify your distribution

## Slide 32: Distribution of parameters
Example Luangwa: constraining on evaporation
Winsemius et. al, HESS, 2008

## Slide 33: Distribution of parameters
Example Luangwa: methodology

## Slide 34: Distribution of parameters
Example Luangwa: Results

## Slide 35: Distribution of parameters
Example Luangwa: distributed responses

## Slide 36: Distribution of parameters
How to limit equifinality in distributed models?
Transfer function methods:
  Lookup tables or functions to link model parameters with soil types, land cover classes
Equifinality

## Slide 37: Distribution of parameters
How to limit equifinality in distributed models?
Transfer function methods:
  Lookup tables or functions to link model parameters with soil types, land cover classes
Use constraints
Equifinality
  Parameter constraints:
  Imax, grass < Imax, forest
  Sumax, wetland < Sumax, plateau
  Process constraints:
  Qdry, fast, hillslope < Q dry, fast, wetland
  Qdry, fast, hillslope < Q dry, fast, wetland

## Slide 38: Distribution of model structure
Parallel modelling

## Slide 39: Distribution of model structure
Classification required
  Topography
  Land use
  Subsurface
Only dominant runoff processes for a each class
Processes occur simultaneously
Limited connections between neighbouring classes
  Possible connection via groundwater reservoir
Parallel modelling

## Slide 40: Distribution of model structure
Parallel modelling: FLEX-Topo
Gao, HESS, 2014
Distance from stream
Height above stream

## Slide 41: Distribution of model structure
Parallel modelling: FLEX-Topo

## Slide 42: Distribution of model structure
Assumptions
  Which processes are dominant
  Boundaries of hydrotopes
Testing is difficult
  No measurements at appropriate scale
  Extra data sources required
  Internal realism checks
    Transferability
Constraining based on expert knowledge can help
Parallel modelling

## Slide 43: Distribution of model structure
Example testing with tracer data
Uhlenbrook et. al, JoH, 2004

## Slide 44: Distribution of model structure
Example testing with tracer data

## Slide 45: Distribution of model structure
Example testing with tracer data

## Slide 46: Data sources
History: from point to grid  geo-statistical interpolation, e.g.
  Thiessen polygons (nearest neighbour)
  Kriging (co-variance matrix approach)
  Inverse distance weighted
  See also: lecture notes hydrological measurements
General problem: by interpolating, you loose (local) extremes
Introduction

## Slide 47: Data sources
Now:
Remote sensors on satellites provide new data:
  … to used distributed input data,
  … to help estimating parameters,
  … to support distributed models.
Introduction

## Slide 48: Data sources
Elevation
Hydrosheds
http://hydrosheds.cr.usgs.gov/dataavail.php
Usage:
Slopes
HAND
Drain direction
Catchment delineation

## Slide 49: Data sources
HAND (Height Above Nearest Drain)
height almost equal to stream height
large height difference with stream

## Slide 50: Data sources
HAND (Height Above Nearest Drain)
http://global-hand.appspot.com/

## Slide 51: Data sources
Many rainfall products available
  Eobs (0.25x0.25 º, daily, for Europe, KNMI data centre)
  http://www.ecad.eu/download/ensembles/ensembles.php
  Tropical Rainfall Measuring Mission (TRMM, ~25x25 km, 3-hourly)
  http://pmm.nasa.gov/TRMM
  GPM (since 2014)
  http://pmm.nasa.gov/data-access/downloads/gpm
  GSMaP (~10x10 km, 1-hourly)
  FEWS RFE 2.0 (10x10 km, daily)
  PERSIANN CCS (4x4 km, 30-min!!)
Rainfall

## Slide 52: Data sources
Rainfall

## Slide 53: Data sources
Validation and bias-correction is often required!!
Rainfall

## Slide 54: Data sources
Globcover
http://due.esrin.esa.int/page_globcover.php
Corine
http://www.eea.europa.eu/data-and-maps/figures/corine-land-cover-types-2006
Usage:
Delineation of response units
Estimation of parameters
Land cover

## Slide 55: Data sources
‘Greenness’ of the area
http://e4ftl01.cr.usgs.gov/MOLT/MOD13A1.005/
Usage:
Proxy for transpiration
Constraining of model
Delineation response units
NDVI

## Slide 56: Data sources
Correlation with soil moisture
NDII
Sriwongsitanon, N., et al., HESSD, 2015.

## Slide 57: Data sources
Modis snow
ftp://n5eil01u.ecs.nsidc.org/SAN/MOST/MOD10A1.005
Check for snow modelling
Snow products

## Slide 58: Data sources
Mod16 evaporation
http://www.ntsg.umt.edu/project/mod16
LSA-SAF evaporation
https://landsaf.ipma.pt/;jsessionid=117534FA19A153B092CC5E1EBBCDF747
GLEAM
http://www.gleam.eu/#datasets
SEBAL
Forcing data
Calibration data
Evaporation products

## Slide 59: Data sources
CUASHI
http://data.cuahsi.org/
SWITCH-ON
http://tl-243.xtr.deltares.nl/byod/#/map
GEOSS Portal
http://www.geoportal.org/web/guest/geo_home_stp
Searching for data…

## Slide 60: Data sources
Provide input (e.g. rainfall, (potential) evaporation)
Constrain model structures and parameterization
Mitigating the 'equifinality problem' by incorporating the spatially distributed data in a performance criterium
How to use

## Slide 61: Exercises
Literature exercise:
Write a review